## Slide 1
UV
Texture
Unit
No Texture ( -> white + Semi = 0 )
RGB
888
RGB
999
Interpolate RGB
255=1.0
256=1.0
max 511
*
Clamp ?
Semi Flag (force to 0 if opaque command)
Blend
Unit
Is Transparent : (RGB==0) & !SemiFlag
Blend
Mode
Dither
Stencil
Scissor
Pixel inside Draw Area (SCISSOR)
Clamp
Min(V,255)
Min(V,255)
Max(V,0)
Not sure
Reduce
17 bit -> 9 bit
[16:8]
Clamp -> [7:0]
No Clamp -> [8:0]
Inside Primitive command
On/Off
Dither
Tex Window
Reg
RAM read/write
Blend On/Off
Inside Primitive command
X0/Y0/X1/Y1 Registers
Tex Base X/Y Tex Format Tex Disable Tex X/Y Flip
Offset X/Y
#
# : Convert 999 to 666 in OLD GPU (Basically do 999->666->999 here)
Test On/Off Write On/Off
Notes: 1/ If texture RGB = 000, then multiplied result is also 000, so no problem of false color.
2/ RGB = 000 MUST be done at texture unit, not post multiply. Interpolated color x 0 should not created transparent pixels !
3/ Primitive bounding box optimize scanning and memory access. Question :
4/ Dithering should happen just before pixel write. (after blending) ??? Do we dither BEFORE blending unit (makes no sense after to do again 888 compute)
5/ Clamp post multiply is only checking for overflow post Mul (because interpolate can be up to 511/256)
But if we put clamp here, we MUST also have overflow/underflow POST blend (ie additive, substractive result). Do we need Clamp post reduce ?

## Slide 2
Interpolate
RGB
Interpolate
UV
Tex Window
Reg
Tex Base X/Y Tex Format Tex Disable Tex X/Y Flip
Valid Pixel
Inside Primitive
& Stencil OK (no stencil or mask=1)
Next
Needed to WAIT for CLUT
or TEX CACHE or other (FIFO ? WriteBack ?)
TEX$
X[1:0] / Y[1:0] for dither
CLUT$
Pipe if TRUE
COLOR
Next = Tex$Hit & Clut$Hit
Tex$Hit = Real Hit | TexDisable | Invalid Pixel
Clut$Hit = Real Hit | TrueColor | Invalid Pixel
1/ If Tex out not found, UV and RGB won’t change
-> Force to read Tex$ until data updated.
2/ On Tex$ HitMiss Transition for both valid pixel.
We kick a TEX$ cache update read.
Same with Clut$